## Slide 1
Chapter 1
Computer Abstractions and Technology

## Slide 2: Understanding Performance
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed
per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed
Notes: Until the 8th slide it’s not important

## Slide 3: Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to
machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers
§1.2 Below Your Program

## Slide 4: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 5: Components of a Computer
Same components for all kinds of computer
  Desktop, server,
embedded
Input/output includes
  User-interface devices
    Display, keyboard, mouse
  Storage devices
    Hard disk, CD/DVD, flash
  Network adapters
    For communicating with other computers
§1.3 Under the Covers
The BIG Picture

## Slide 6: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface
  The ISA plus system software interface
Implementation
  The details underlying and interface
The BIG Picture

## Slide 7: Defining Performance
Which airplane has the best performance?
Boeing 777
Boeing 747
BAC/Sud Concorde
Douglas DC-8-50
0 100 200 300 400 500
Passenger Capacity
Boeing 777
Boeing 747
BAC/Sud Concorde
Douglas DC- 8-50
0 2000 4000 6000 8000 10000
Cruising Range (miles)
0
500 1000
1500
Boeing 777
Boeing 747
BAC/Sud Concorde
Douglas DC-8-50
Cruising Speed (mph)
0
100000 200000 300000 400000
Boeing 777
Boeing 747
BAC/Sud Concorde
Douglas DC- 8-50
Passengers x mph
§1.4 Performance

## Slide 8: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…

## Slide 9: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
PerformanceX PerformanceY
 Execution timeY Execution timeX  n
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA
= 15s / 10s = 1.5
  So A is 1.5 times faster than B
Notes: These rules are important to understand and practice it

## Slide 10: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance
Notes: Elapsed : المنقضي

## Slide 11: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock period
Clock (cycles)
Data transfer and computation
Update state
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 12: CPU Time
CPU Time  CPUClock Cycles Clock Cycle Time
 CPUClock Cycles Clock Rate
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count
Notes: This rule important to understand and practice and dealing with it

## Slide 13: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?
6s 6s
Clock Rate
CPU TimeB 6s
B
  4GHz
1.2  20109 24109
Clock RateB 
Clock CyclesA  CPU TimeA Clock RateA
 10s 2GHz  20109
 Clock CyclesB  1.2 Clock CyclesA

## Slide 14: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix
ClockCycles  Instruction Count Cyclesper Instruction
CPUTime Instruction Count CPIClockCycle Time
 Instruction Count CPI
ClockRate

## Slide 15: CPI Example
CPUTim eB  I 600ps  1.2 CPUTim eA I 500ps
CPUTim eB  Instruction Count CPIB Cycle Tim eB
 I1.2 500ps I 600ps
 I 2.0 250ps I 500ps
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
CPUTim eA  Instruction Count CPIA Cycle Tim eA
A is faster…
…by this much
Notes: We discussed about how to calculate the performance in previous slide

## Slide 16: CPI in More Detail
If different instruction classes take different numbers of cycles
n
Clock Cycles  (CPIi Instruction Counti )
i1
Weighted average CPI




n
 
i1 
i
i
Instruction Count 
Instruction Count
CPI 
Clock Cycles Instruction Count
CPI 
Relative frequency

## Slide 17: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles
= 2×1 + 1×2 + 2×3
= 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
Clock Cycles
= 4×1 + 1×2 + 1×3
= 9
Avg. CPI = 9/6 = 1.5

## Slide 18: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture
Seconds Clock cycle
CPU Time  Instructions  Clock cycles 
Program Instruction

## Slide 19: SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2006
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Normalize relative to reference machine
  Summarize as geometric mean of performance ratios
    CINT2006 (integer) and CFP2006 (floating-point)
n
n Execution timeratioi i1

## Slide 20: CINT2006 for Opteron X4 2356
Name | Description | IC×109 | CPI | Tc (ns) | Exec time | Ref time | SPECratio
perl | Interpreted string processing | 2,118 | 0.75 | 0.40 | 637 | 9,777 | 15.3
bzip2 | Block-sorting compression | 2,389 | 0.85 | 0.40 | 817 | 9,650 | 11.8
gcc | GNU C Compiler | 1,050 | 1.72 | 0.47 | 24 | 8,050 | 11.1
mcf | Combinatorial optimization | 336 | 10.00 | 0.40 | 1,345 | 9,120 | 6.8
go | Go game (AI) | 1,658 | 1.09 | 0.40 | 721 | 10,490 | 14.6
hmmer | Search gene sequence | 2,783 | 0.80 | 0.40 | 890 | 9,330 | 10.5
sjeng | Chess game (AI) | 2,176 | 0.96 | 0.48 | 37 | 12,100 | 14.5
libquantum | Quantum computer simulation | 1,623 | 1.61 | 0.40 | 1,047 | 20,720 | 19.8
h264avc | Video compression | 3,102 | 0.80 | 0.40 | 993 | 22,130 | 22.3
omnetpp | Discrete event simulation | 587 | 2.94 | 0.40 | 690 | 6,250 | 9.1
astar | Games/path finding | 1,082 | 1.79 | 0.40 | 773 | 7,020 | 9.1
xalancbmk | XML parsing | 1,058 | 2.70 | 0.40 | 1,143 | 6,900 | 6.0
Geometric mean |  |  |  |  |  |  | 11.7
High cache miss rates

## Slide 21: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
§1.8 Fallacies and Pitfalls
20  80  20
n
Can’t be done!
unaffected
improvement factor
Taffected
T
Timproved 
Example: multiply accounts for 80s/100s
  How much improvement in multiply performance to get 5× overall?
Corollary: make the common case fast
Notes: If you don’t understand the slides in notes he explain it easier in page 11

## Slide 22: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance
§1.9 Concluding Remarks