## Slide 1
Chapter 2
Instructions: Language of the Computer

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction

## Slide 3: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E
Notes: MIPS: this is the CPU we will study his instruction .

## Slide 4: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 5: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 6: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware

## Slide 7: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add | $t0, | $s1, | $s2
add | $t1, | $s3, | $s4
sub | $s0, | $t0, | $t1

## Slide 8: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 9: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 10: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw | $t0, | 32($s3) | # | load | word
add | $t0, | $s2, $t0 |  |  | 
sw | $t0, | 48($s3) | # | store | word
Notes: Note That we don’t need to use save variable register

## Slide 11: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 12: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 13: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
add $t2, $s1, $zero

## Slide 14: Unsigned Binary Integers
Given an n-bit number
1 0
x  x 2
n1 n2
n1 n2 1 0
 x 2  x 2  x 2
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112
= 0 + … + 1×23 + 0×22 +1×21 +1×20
= 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers

## Slide 15: 2s-Complement Signed Integers
Given an n-bit number
0
1 0
2
n1 n2 1
x  xn12  xn2 2  x 2  x
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002
= –1×231 + 1×230 + … + 1×22 +0×21 +0×20
= –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 16: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 17: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
x  x  1111...1112  1
x  1 x
Example: negate +2
 +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1
= 1111 1111 … 11102

## Slide 18: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
 +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 19: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23
§2.5 Representing Instructions in the Computer
Notes: The number of registers save it in worse case .

## Slide 20: MIPS R-format Instructions
op | rs | rt | rd | shamt | funct
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)

## Slide 21: R-format Example
add $t0, $s1, $s2
special | $s1 | $s2 | $t0 | 0 | add
0 | 17 | 18 | 8 | 0 | 32
000000 | 10001 | 10010 | 01000 | 00000 | 100000
000000100011001001000000001000002 = 0232402016
op | rs | rt | rd | shamt | funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 22: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 23: MIPS I-format Instructions
op | rs | rt | constant or address
6 bits 5 bits 5 bits 16 bits
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible

## Slide 24: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 25: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations
Notes: You must understand this slide very well

## Slide 26: Shift Operations
op | rs | rt | rd | shamt | funct
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)

## Slide 27: AND Operations
0000 0000 0000 0000 000 | 0 110 | 1 1100 0000
0000 0000 0000 0000 00 | 11 110 | 0 0000 0000
0000 0000 0000 0000 000 | 0 110 | 0 0000 0000
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
$t2
$t1
$t0

## Slide 28: OR Operations
0000 0000 0000 0000 000 | 0 110 | 1 1100 0000
0000 0000 0000 0000 00 | 11 110 | 0 0000 0000
0000 0000 0000 0000 00 | 11 110 | 1 1100 0000
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
$t2
$t1
$t0

## Slide 29: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 30: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1
§2.7 Instructions for Making Decisions

## Slide 31: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
$s4, Else
$s1, $s2
bne $s3, add $s0, j Exit sub $s0,
…
Else: Exit:
$s1, $s2
Assembler calculates addresses

## Slide 32: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: | sll | $t1, | $s3, | 2
 | add | $t1, | $t1, | $s6
lw |  | $t0, | 0($t1) | 
bne |  | $t0, | $s5, Exit | 
addi |  | $s3, | $s3, 1 | 
j |  | Loop |  | 
Exit: … |  |  |  | 

## Slide 33: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
    A compiler identifies basic blocks for optimization
    An advanced processor can accelerate execution of basic blocks

## Slide 34: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
slt $t0, $s1,
bne $t0,
$zero, L
$s2 # if ($s1 < $s2)
# branch to L

## Slide 35: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise

## Slide 36: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 37: Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)

## Slide 38: Branch Addressing
op | rs | rt | constant or address
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
6 bits 5 bits 5 bits 16 bits
  PC-relative addressing
    Target address = PC + offset × 4
    PC already incremented by 4 by this time
Notes: We also take about it important information in the note in next slide.

## Slide 39: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
op
address
6 bits
26 bits
(Pseudo)Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 40: Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll | $t1, | $s3, 4 | 80000 | 0 | 0 | 19 | 9 | 4 | 0
add | $t1, | $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw | $t0, | 0($t1) | 80008 | 35 | 9 | 8 |  | 0 | 
bne | $t0, | $s5, Exit | 80012 | 5 | 8 | 21 |  | 2 | 
addi | $s3, | $s3, 1 | 80016 | 8 | 19 | 19 |  | 1 | 
j | Loop |  | 80020 | 2 |  | 20000 |  |  | 
Exit: … |  |  | 80024 |  |  |  |  |  | 

## Slide 41: Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler rewrites the code
Example
beq $s0,$s1, L1
↓
bne $s0,$s1, L2 j L1
L2: …

## Slide 42: Addressing Mode Summary
Notes: The Doctor did not stop on this slide but you must understand it

## Slide 43: Effect of Compiler Optimization
3
2.5
2
1.5
1
0.5
0
none
O1
O2
O3
Relative Performance
180000
160000
140000
120000
100000
80000
60000
40000
20000
0
none
O1
O2
O3
Clock Cycles
140000
120000
100000
80000
60000
40000
20000
0
none
O1
O2
O3
Instruction count
0
0.5
1
1.5
2
none
O1
O2
O3
CPI
Compiled with gcc for Pentium 4 under Linux

## Slide 44: Effect of Language and Algorithm
3
2.5
2
1.5
1
0.5
0
C/none
C/O1
C/O2
C/O3
Java/int
Java/JIT
Bubblesort Relative Performance
2
1.5
1
0.5
0
2.5
C/none
C/O1
C/O2
C/O3
Java/int
Java/JIT
Quicksort Relative Performance
3000
2500
2000
1500
1000
500
0
C/none
C/O1
C/O2
C/O3
Java/int
Java/JIT
Quicksort vs. Bubblesort Speedup

## Slide 45: Lessons Learnt
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
Nothing can fix a dumb algorithm!

## Slide 46: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less
productivity
§2.18 Fallacies and Pitfalls

## Slide 47: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accrete more instructions
x86 instruction set

## Slide 48: Pitfalls
Sequential words are not at sequential addresses
  Increment by 4, not by 1!
Keeping a pointer to an automatic variable after procedure returns
  e.g., passing pointer back via an argument
  Pointer becomes invalid when stack popped

## Slide 49: Concluding Remarks
Design principles
  Simplicity favors regularity
  Smaller is faster
  Make the common case fast
  Good design demands good compromises
Layers of software/hardware
Compiler, assembler, hardware
MIPS: typical of RISC ISAs
  c.f. x86
§2.19 Concluding Remarks

## Slide 50
 | Concluding Remarks |  |  |  | 
 | Measure MIPS instruction executions in benchmark programs Consider making the common case fast Consider compromises |  |  |  | 
In | struction class | MIPS examples | SPEC2006 Int | SPEC2006 FP | 
 | Arithmetic | add, sub, addi | 16% | 48% | 
 |  | lw, sw, lb, lbu, lh, lhu, sb, lui | 35% | 36% | 
Data transfer |  |  |  |  | 
Logical |  | and, or, nor, andi, ori, sll, srl | 12% | 4% | 
Cond. Branch |  | beq, bne, slt, slti, sltiu | 34% | 8% | 
Jump |  | j, jr, jal | 2% | 0% |